## Slide 1: Verilog HDL (Intro & Structural)
Meisam Abdollahi
School of Computer Engineering
Iran University of Science and Technology
meisam.abdolahi@ut.ac.ir
Winter 1400 (Computer Aided Design)

## Slide 2: RTL Design
RTL is the abstraction level between algorithm and logic gates.
A circuit is described in terms of registers (flip-flops or latches) and the data is transferred between them using logical operations

## Slide 3: Transaction Level Modeling
Transaction Level Modeling (TLM) is a technique for describing a system by using function calls that define a set of transactions over a set of channels.
TLM descriptions can be more abstract, and therefore simulate more quickly than the RTL.
Evaluation the performances and the behavior of the IP very early in the design flow

## Slide 4: RTL vs. TLM
System Verilog
Verilog
System C
VHDL

## Slide 5: Verilog - HDL
Verilog Introduction
Supports structural and behavioral descriptions
Structural
  Explicit structure of the circuit
  How a module is composed as an interconnection of more primitive modules/components
  E.g., each logic gate instantiated and connected to others
Behavioral
  Program describes input/output behavior of circuit
  Many structural implementations could have same behavior
  E.g., different implementations of one Boolean function

## Slide 6: Verilog Structural models of combinational Logic
Module
A module is the basic building block in Verilog.
A module can be an element or a collection of lower-level design blocks.
A module provides the necessary functionality to the higher-level block through its port interface (inputs and outputs), but hides the internal implementation.
module ModuleName [(Port,...)];
ModuleItems...
endmodule
The name of Module
The Port
Interface List
The Body of Module
Represents the internal description of the module

## Slide 7
Identifiers
Identifiers are the names you give your Modules, wires, gates, functions, and anything else you design or use.
The basic rules for identifiers are as follows:
May contain letters (a-z, A-Z), digits (0-9), underscores (_), and dollar signs ($).
Must start with a letter or underscore.
Are case sensitive (unless made case insensitive by a tool option).
May be up to 1024 characters long.
Other printable ASCII characters may be used in an escaped identifier.
Names in Verilog are case sensitive
The language uses certain keywords, all of which must use lowercase characters.
Verilog Structural models of combinational Logic
Notes: Escaped identifiers begin with a backslash and end with a space character.

## Slide 8
Comments
Comments may appear anywhere in a Verilog source text.
A comment designator starting with // makes the rest of the line, up to a new-line character, a comment.
The symbols /* and */ bracket a section of code as a comment, and they go across new-line characters.
Verilog Structural models of combinational Logic

## Slide 9
Ports
The ports of modules model the pins or edge connectors of hardware components.
Each port in the port list is defined as input, output or inout, based on the direction of the port signal.
Ports can be declared as follows:
  Port declaration:
  input [range] name
  output [range] name
  inout [range] name
Verilog Structural models of combinational Logic

## Slide 10
example
module Reg_8bit (Din, clr, clk, Dout);
// Port Declaration Section
input clk,clr;
input [0:7] Din;
Output [0:7] Dout;
// module internals
...
endmodule
module Reg_8bit (input [0:7] Din,
input clr, clk,
output [0:7] Dout);
// module internals
...
endmodule
Port Definition
Port Declaration
Port Definition & Declaration
Verilog Structural models of combinational Logic

## Slide 11
Logic Values
Verilog wires and variables take the 4-value logic value system
Values in this system are 0, 1, Z, and X.
0 :
Forcing 0 like a direct pull to the ground
Resistive 0 is generated when there is a large resistance between a line and a forcing 0 value
Capacitive 0 is when a line is float; but has a capacitance that has a zero charge.
Verilog-Logical Values

## Slide 12
Logic Values
Verilog wires and variables take the 4-value logic value system
Values in this system are 0, 1, Z, and X.
Verilog-Logical Values
1 :
Forcing 1 like a direct pull to the VCC (Power Supply)
Resistive 1 is generated when there is a large resistance between a line and a forcing 1 value
Capacitive 1 is when a line is float; but has a capacitance that has a VCC charge.

## Slide 13
Logic Values
Verilog wires and variables take the 4-value logic value system
Values in this system are 0, 1, Z, and X.
Verilog-Logical Values
Z :
The Z value represents an undriven, high-impedance value. This is the electrical float which causes no current flow to either supply or ground voltage.
Both Z and z are acceptable forms of this logic value

## Slide 14
Logic Values
Verilog wires and variables take the 4-value logic value system
Values in this system are 0, 1, Z, and X.
Verilog-Logical Values
X :
The X value represents a conflict in multiple driving values, an unknown, an uninitialized value, a short between two opposing values (0 and 1), or a bus contention.
Driven wires and Verilog variables assume X for their initial values
Both X and x are acceptable forms of this logic value

## Slide 15
Primitive Gates
A number of primitives, or Gates, are built into the Verilog language. They represent basic logic gates (e.g. and, or).
Verilog Structural models of combinational Logic

## Slide 16
Primitive Gates (cont.)
Verilog Structural models of combinational Logic

## Slide 17
Primitive Gates (cont.)
Verilog Structural models of combinational Logic

## Slide 18
Primitive Gates (cont.)
Verilog Structural models of combinational Logic

## Slide 19
Verilog Structural Model using Primitive Gates
module AOI_1 (y_out , x_in1 , x_in2 , x_in3 , x_in4 , x_in5);
output y_out;
input x_in1 , x_in2 , x_in3 , x_in4 , x_in5;
wire y1 , y2;
nor (y_out , y1 , y2);
and (y1 , x_in1 , x_in2);
and (y2 , x_in3 , x_in4 , x_in5);
endmodule
Nets (sometimes called wires) are the most common data object in Verilog. Nets are used to interconnect modules and primitives

Verilog Structural models of combinational Logic

## Slide 20
Verilog Data Types
Nets : Establish structural connectivity. A net represents a hardware wire driven by one or more gates or other types of signal sources.
There are two Data Types in Verilog HDL :
net
Variable
Net Data types :
wire
tri
wand
wor
triand
trior
supply0
supply1
tri0
tri1
trireg
Verilog-Data Types

## Slide 21
Verilog Data Types
Nets :
The net data types can represent physical connections between structural entities, such as gates.
it does not store values. It must be driven by something, and cannot store a value without being driven.
its value is determined by the values of its drivers, such as a continuous assignment or a gate.
There are two Data Types in Verilog HDL :
net
Variable
Net Data types :
wire
tri
wand
wor
triand
trior
supply0
supply1
tri0
tri1
trireg
Verilog-Data Types

## Slide 22
wire: establish connectivity, with no logical behavior or functionality implied.
tri: establish connectivity, with no logical behavior or functionality implied. Same as wire but is identified to indicate that it will be three-stated in hardware. ( tri wire )
Net Types:
Verilog-Data Types
Notes: There is no difference between wire and tri. They are synonyms.
Usually the convention is to use wire in regular declaration and tri in declaration of multiple-driven nets and inout ports.

## Slide 23
wand: a net that is connected to the output of multiple primitives. It models the hardware implementation of a wired-AND, e.g. open collector tech.
triand: a net that is connected to the output of multiple primitives. It models the hardware implementation of a wired-AND, e.g. open collector tech. The physical net is to be three-stated. ( triand wand )
Net Types:
Verilog-Data Types

## Slide 24
wor: a net that is connected to the output of multiple primitives. It models the hardware implementation of a wired-OR, e.g. open collector tech.
trior: a net that is connected to the output of multiple primitives. It models the hardware implementation of a wired-OR, e.g. open collector tech. The physical net is to be three-stated. ( trior wor )
Net Types :
Verilog-Data Types

## Slide 25
tri0: a net that is connected to GND by resistive pull-down connection.
tri1: a net that is connected to the Power supply by a resistive pull-up.
Net Types:
Verilog-Data Types
Notes: When a net has no drivers, or all driving Z, a tri1 net will get pulled to the 1 state.

## Slide 26
supply0: a global net that is connected to GND.
supply1: a global net that is connected to Power Supply.
trireg: The trireg type net behaves as a capacitive wire and holds its old value when a new resolved value is to become Z.
Net Types:
Verilog-Data Types

## Slide 27
Variable Data Type:
The variable data type is an abstraction of a data storage element.
A variable shall store a value from one assignment to the next.
Register Data types :
reg
integer
real
real time
time
Verilog-Data Types

## Slide 28
Variable Type:
reg: this type is an abstraction of a hardware storage element, but it dose not corresponding directly to physical memory.
A reg variable has a default value of x.
The default size of a register variable is single bit.
Verilog operators create a reg variables as an unsigned value.
A register variable may be assigned value only by procedural statement (behavioral description)
Verilog-Data Types

## Slide 29
Variable Type:
integer: this type supports numeric computation in procedural statements.
  Integers are represented internally to the word length of the host machine ( at least 32 bits )
  An integer variable has a default initial value 0.
real : real are stored in double precision, typically a 64-bit. A real variable has a default initial value of 0.0. Real variables can be specified in decimal and exponential notation.
Verilog-Data Types

## Slide 30
Variable Type:
realtime: simply stores time as a floating point quantity. A realtime variable has a default initial value of 0.0.
Time: is an unsigned 64-bit quantities and used to store simulation time. A variable of type time may not be used in a module port, nor may it be an input or output of a primitive. A time variable has a default value of 0.
Verilog-Data Types

## Slide 31
Two types of net strengths are drive_strength and charge_strength.
Net Strength:
Strengths of a net used as a switch input affect the strength of the output of the switch.
Strengths of several signals driving a net, affect the way net logic values are resolved.
Verilog-Data Types

## Slide 32
Net Strength :
wand (pull0, supply1) sim;
Verilog-Data Types

## Slide 33
The strength of storage nets specify how weak or strong the charge capability of the net is.
Three strength values, large, medium, and small are used for these net types, and the default is medium.
trireg (small) cap1;
Net Strength :
Verilog-Data Types

## Slide 34
Strength values are instrumental in deciding logic values of signals with multiple drivers.
If a net has multiple drivers of the same strength values, its net type, i.e., wire, wand, or wor decides on the final value of the net.
If drive strengths of multiple drivers of a net are different, conflicts are resolved by taking the logic value that has a higher strength.
  In this case, resolution type of the net (i.e., wire, wand, or wor) does not play any role in determining the net value.
Strength used in resolution:
Verilog-Data Types

## Slide 35
module wired_strength (input a, b, output z1, z2, z3);
wire y1;
wand y2;
wor y3;
buf (pull1, weak0) (y1, a);
buf (pull1, weak0) (y1, b);
buf (pull1, weak0) (y2, a);
buf (pull1, supply0) (y2, b);
buf (pull1, weak0) (y3, a);
buf (Strong1, weak0) (y3, b);
assign z1 = y1;
assign z2 = y2;
assign z3 = y3;
endmodule
Example:
Verilog-Data Types

## Slide 36
Port connection Rules
Outputs: Internally, output ports can be of the type reg or net. Externally, outputs must always be connected to a net. They cannot be connected to a reg.
Inputs: Internally, input ports must always be of the type net. Externally, the inputs can be connected to a variable which is a reg or net.
Inouts: Internally, inout ports must always be of the type net. Externally, inout ports must always be connected to a net.
Verilog Structural models of combinational Logic

## Slide 37: Modeling Hardware
The biggest difficulty is representing concurrently operating hardware.
It is needed to “simulate” the execution of several parts of the circuit at the same time.
Verilog models combinational circuits by what are called concurrent statements
  These statements are evaluated any time and every time a signal on the right side of the statement changes.

## Slide 38: Concurrent Statement
The Verilog simulator monitors the right side of each concurrent statement, and any time a signal changes, the expression on the right side is immediately reevaluated after the defined delay.
The order is not importnat
Optional

## Slide 39
Top Down Design and Nested Modules
Verilog Structural models of combinational Logic

## Slide 40
Top Down Design and Nested Modules
Verilog Structural models of combinational Logic

## Slide 41
Top Down Design and Nested Modules
module Half_Adder(sum , cout , a , b);
input a , b;
output sum , cout;
xor (sum , a , b);
and (cout , a , b);
endmodule
outputs are of wire type by default
Verilog Structural models of combinational Logic

## Slide 42
Top Down Design and Nested Modules
module Full_Adder (sum , c_out , a , b , c_in );
output sum, c_out;
input a, b, c_in;
wire w1 , w2 , w3;
Half_Adder M1 (w1 , w2 , a , b);
Half_Adder M2 (sum , w3 , c_in , w1);
or (c_out , w2 , w3);
endmodule
Verilog Structural models of combinational Logic

## Slide 43
Top Down Design and Nested Modules
module RCA_Adder_4(sum,
cout,
a, b,
cin);
output [3: 0] sum;
output cout;
input [3: 0] a, b;
input cin;
wire cin1, cin2, cin3;
Full_Adder M1 (sum[0], cin1, a[0], b[0], cin);
Full_Adder M2 (sum[1], cin2, a[1], b[1], cin1);
Full_Adder M3 (sum[2], cin3, a[2], b[2], cin2);
Full_Adder M4 (sum[3], cout, a[3], b[3], cin3);
endmodule
Verilog Structural models of combinational Logic