## Slide 1: VHDL (Data Types)
Meisam Abdollahi
School of Computer Engineering
Iran University of Science and Technology
meisam.abdolahi@ut.ac.ir
Winter 1400 (Computer Aided Design)

## Slide 2: Data Types (I)
Types
Access
Composite
Array
Record
Scalar
Integer
Real
Enumerated
Physical
Boolean
Character
Bit
Std_logic
(equivalent to pointers in C)
allows dynamic memory allocation

## Slide 3: Data Types (II)
Scalar Types
  Integer Type
    Minimum range for any implementation as defined by standard:
    -2,147,483,647 to 2,147,483,647
  Real Type [Simulation only]
    Minimum range for any implementation as defined by standard: -1.0E38 to 1.0E38
  Boolean Type
    It has two values of “True” and “False”
  Character type [Simulation only]
    It supports all characters such as ‘a’..’z’, ‘[‘, ‘{‘ and etc.
  Bit type
    It has two values of ‘1’ and ‘0’
  Std_logic type
    It is IEEE standard
    contain: ‘U’, ‘X’, ‘0’, ‘1’, ‘Z’, ‘w’, ‘L’, ‘H’, ‘-’

## Slide 4: STD_LOGIC
STD_LOGIC is defined in the library std_logic_1164.This is a nine valued logic system.
  It has 9 values: 'U', 'X', '0', '1', 'Z', 'W', 'L' ,'H' and '-’. The meaning of each of these characters are:
    U = uninitialized [Simulation only] X = unknown - a multisource line is driven '0' and '1' simultaneously [synthesizable] 0 = logic 0 [synthesizable] 1 = logic 1 [synthesizable] Z = high impedance (tri state) [synthesizable] W = weak unknown [Simulation only] L = weak ‘0’[Simulation only] H = weak ‘1’[Simulation only] - = don't care [Simulation only]

## Slide 5: Data Types (III)
Some examples
  x0 <= '0'; -- bit or std_logic gets '0‘
  x1 <= "00011111"; -- bit_vector, std_logic_vector, signed, or unsigned
  x2 <= "0001_1111"; -- underscore allowed to ease visualization
  x3 <= "101111" -- binary representation of decimal 47
  x4 <= B"101111" -- binary representation of decimal 47
  x6 <= X"2F" -- hexadecimal representation of decimal 47
  n <= 1200; -- integer
  m <= 1_200; -- integer, underscore allowed
  IF ready THEN... -- Boolean, executed if ready=TRUE
  y <= 1.2E-5; -- real, not synthesizable

## Slide 6: Data Types (IV)
Example: Legal and illegal operations between data of different types
SIGNAL a: BIT;
SIGNAL b: BIT_VECTOR(7 DOWNTO 0);
SIGNAL c: STD_LOGIC;
SIGNAL d: STD_LOGIC_VECTOR(7 DOWNTO 0);
SIGNAL e: INTEGER RANGE 0 TO 255;
...
a <= b(5);
b(0) <= a;
c <= d(5);
d(0) <= c;
a <= c;
b <= d;
e <= b;
e <= d;
-- legal (same scalar type: BIT)
-- legal (same scalar type: BIT)
-- legal (same scalar type: STD_LOGIC)
-- legal (same scalar type: STD_LOGIC)
-- illegal (type mismatch: BIT x STD_LOGIC)
-- illegal (type mismatch: BIT_VECTOR x STD_LOGIC_VECTOR)
-- illegal (type mismatch: INTEGER x BIT_VECTOR)
-- illegal (type mismatch: INTEGER x STD_LOGIC_VECTOR)

## Slide 7: Data Types (III)
Scalar Types (cntd.)
  Enumerated Types [synthesizable]
    A type whose values are defined by listing (enumerating) them explicitly.
    Mostly state machines use it
    Example:
  Physical Types: [Simulation only]
    A numeric type for representing some physical quantity, such as mass, length, time or voltage.
Type state_type is (start, idle, waiting, run)
Signal state: state_type;
TYPE resistence IS RANGE 0 to 1000000
UNITS
ohm; -- ohm
Kohm = 1000 ohm; -- 1 K
Mohm = 1000 kohm; -- 1 M
END UNITS;

## Slide 8: Data Types (IV)
  Physical type (cntd.) [Simulation only]
  Time units are the only predefined physical type in VHDL
TYPE TIME IS RANGE -2147483647 to 2147483647
UNITS
fs; -- femtosecond
ps = 1000 fs; -- picosecond
ns = 1000 ps; -- nanosecond
us = 1000 ns; -- microsecond
ms = 1000 us; -- millisecond
sec = 1000 ms; -- second
min = 60 sec; -- minute
hr = 60 min; -- hour
END UNITS;

## Slide 9: User-Defined Data Types
VHDL also allows the user to define his/her own data types
  TYPE my_integer IS RANGE -32 TO 32;
  -- A user-defined subset of integers.
  TYPE student_grade IS RANGE 0 TO 100;
  -- A user-defined subset of integers or naturals.
  Enumerated Types
    TYPE color IS (red, green, blue, white);
      -- Another enumerated data type.

## Slide 10: Data Types (VIII)
Subtype
  A type with a constraints
  Assignments that are out of the subtype range result in an error
  Main reason for using a subtype rather than specifying a new type
    Though operations between data of different types are not allowed, they are allowed between a subtype and its corresponding base type
  Example
    Subtype my_int is integer range 0 to 3215;
    subtype byte1 is std_logic_vector(7 downto 0);
    SUBTYPE my_logic IS STD_LOGIC RANGE '0' TO 'Z';
    -- Recall that STD_LOGIC=('X','0','1','Z','W','L','H','-').
    -- Therefore, my_logic=('0','1','Z').

## Slide 11: Data type (An example)
Which one is legal and which one is illegal
SUBTYPE my_logic IS STD_LOGIC RANGE '0' TO '1';
SIGNAL a: BIT;
SIGNAL b: STD_LOGIC;
SIGNAL c: my_logic;
...
b <= a;
b <= c;
--illegal (type mismatch: BIT versus STD_LOGIC)
--legal (same "base" type: STD_LOGIC)

## Slide 12: Data Types (Array I)
Composite Types
  Array Types:
    Used to collect one or more elements of a similar type in a single construct
    Elements can be any VHDL data type
    They can be one-dimensional (1D), two-dimensional (2D), or one-dimensional-by-one-dimensional (1Dx1D).
    Other dimensions are possible, but NOT synthesizable

## Slide 13: Data Types (Array II)
(a): scalar (single bit)
(b) 1D also called vector
(c) 1Dx1D
(d) 2D
Predefined Scalars: BIT, STD_LOGIC, and BOOLEAN
Predefined Vectors: BIT_VECTOR, STD_LOGIC_VECTOR, INTEGER, SIGNED, and UNSIGNED
[synthesizable]
[synthesizable]

## Slide 14: Data Types (Array III)
There are no pre-defined 2D or 1Dx1D arrays
  must be specified by the user
To do so, the new TYPE must first be defined
The new SIGNAL, VARIABLE, or CONSTANT can be declared using that data type
To make use of the new array type:
TYPE type_name IS ARRAY (specification) OF data_type;
SIGNAL signal_name: type_name [:= initial_value];

## Slide 15: Data Types (Array IV)
Example: 1Dx1D array
Alternative way
TYPE row IS ARRAY (7 DOWNTO 0) OF STD_LOGIC; -- 1D array
TYPE matrix IS ARRAY (0 TO 3) OF row; -- 1Dx1D array
SIGNAL x: matrix; -- 1Dx1D signal
TYPE matrix IS ARRAY (0 TO 3) OF STD_LOGIC_VECTOR(7 DOWNTO 0);

## Slide 16: Data Types (Array V)
Example: 2D array
Example: Array initialization
TYPE matrix2D IS ARRAY (0 TO 3, 7 DOWNTO 0) OF STD_LOGIC;
-- 2D array
... :="0001"; -- for 1D array
... :=('0','0','0','1') -- for 1D array
... :=(('0','1','1','1'), ('1','1','1','0')); -- for 1Dx1D or -- 2D array
0
1
2
3
7
6
5
4
3
2
1
0

## Slide 17: Data Types (Array VI)
Multi-dimensional array (more)
  Example:
    Type data4x8 is array (0 to 3) of std_logic_vector(7 downto 0);
    Type data3x4x8 is array (0 to 2) of data4x8;
    Type truth_table is array(0 to 7, 0 to 4) Of BIT;
    Access of array elements by an example
Architecture rtl of ex is
Signal a_vect : std_logic_vector (4 downto 0)
Begin
A_vect(4)<=‘1’;
A_vect(3 downto 0)<=“0110”;
End rtl;

## Slide 18: Data Types (Array VII)-Example
TYPE row IS ARRAY (7 DOWNTO 0) OF STD_LOGIC; -- 1D array
TYPE array1 IS ARRAY (0 TO 3) OF row; -- 1Dx1D array
TYPE array2 IS ARRAY (3 downto 0) OF STD_LOGIC_VECTOR(7 DOWNTO 0); -- 1Dx1D
TYPE array3 IS ARRAY (0 TO 3, 7 DOWNTO 0) OF STD_LOGIC; -- 2D array
SIGNAL x: row;
SIGNAL y: array1;
SIGNAL v: array2;
SIGNAL w: array3;
x(0) <= y(1)(2); -- notice two pairs of parenthesis -- (y is 1Dx1D)
x(1) <= v(2)(3); -- two pairs of parenthesis (v is 1Dx1D)
x(2) <= w(2,1); -- a single pair of parenthesis (w is 2D)
y(1)(1) <= x(6);
y(2)(0) <= v(0)(0);
y(0)(0) <= w(3,3);
w(1,1) <= x(7);
w(3,0) <= v(0)(3);
Types of scalar assignments- all of them are legal

## Slide 19: Data Types (Array VII)-Example
Vector assignments
x <= y(0);
x <= v(1);
x <= w(2);
x <= w(2, 2 DOWNTO 0);
v(0) <= w(2, 2 DOWNTO 0);
v(0) <= w(2);
y(1) <= v(3);
y(1)(7 DOWNTO 3) <= x(4 DOWNTO 0);
v(1)(7 DOWNTO 3) <= v(2)(4 DOWNTO 0);
w(1, 5 DOWNTO 1) <= v(2)(4 DOWNTO 0);
-- legal (same data types: ROW)
-- illegal (type mismatch: ROW x --STD_LOGIC_VECTOR)
-- illegal (w must have 2D index)
-- illegal (type mismatch: ROW x -- STD_LOGIC)
-- illegal (mismatch: STD_LOGIC_VECTOR -- x STD_LOGIC)
-- illegal (w must have 2D index)
-- illegal (type mismatch: ROW x -- STD_LOGIC_VECTOR)
-- legal (same type, -- same size)
-- legal (same type, -- same size)
-- illegal (type mismatch)
TYPE row IS ARRAY (7 DOWNTO 0) OF STD_LOGIC; -- 1D array
TYPE array1 IS ARRAY (0 TO 3) OF row; -- 1Dx1D array
TYPE array2 IS ARRAY (0 TO 3) OF STD_LOGIC_VECTOR(7 DOWNTO 0); -- 1Dx1D
TYPE array3 IS ARRAY (0 TO 3, 7 DOWNTO 0) OF STD_LOGIC; -- 2D array
SIGNAL x: row;
SIGNAL y: array1;
SIGNAL v: array2;
SIGNAL w: array3;

## Slide 20: Data Types (VII)
Composite Types (contd.)
  Record type
    Used to collect one or more elements of a different types in single construct
    Elements can be any VHDL data type
    Elements are accessed through field name
Architecture beh of ex is
Type data is record
Year: integer range 1996 to 2099;
Month: integer range 1 to 12;
val: std_logic_vector(7 downto 0);
Check: Bit;
End record;
Signal d: data;
Begin
d.year<=2008;
d.month<=4;
d.val<=“01110111”
d.check<=‘1’;
End;

## Slide 21: Data Type (Signed and Unsigned)
These types are defined in the std_logic_arith package of the ieee library.
SIGNAL x: SIGNED (7 DOWNTO 0);
SIGNAL y: UNSIGNED (0 TO 3);
  Notice that their syntax is similar to that of STD_LOGIC_VECTOR
  An UNSIGNED value is a number never lower than zero
  If type SIGNED is used instead, the value can be positive or negative
SIGNED and UNSIGNED data types are intended mainly for arithmetic operations (similar to integer signals)
Unlike std_logic_vector, logical operations are not allowed

## Slide 22: Data Type (Signed and Unsigned)
LIBRARY ieee;
USE ieee.std_logic_1164.all;
USE ieee.std_logic_arith.all; -- extra package necessary
...
SIGNAL a: SIGNED (7 DOWNTO 0);
SIGNAL b: SIGNED (7 DOWNTO 0);
SIGNAL x: SIGNED (7 DOWNTO 0);
...
v <= a + b; -- legal (arithmetic operation OK)
w <= a AND b; -- illegal (logical operation not OK)
LIBRARY ieee;
USE ieee.std_logic_1164.all; -- no extra package required
...
SIGNAL a: STD_LOGIC_VECTOR (7 DOWNTO 0);
SIGNAL b: STD_LOGIC_VECTOR (7 DOWNTO 0);
SIGNAL x: STD_LOGIC_VECTOR (7 DOWNTO 0);
...
v <= a + b; -- illegal (arithmetic operation not OK)
w <= a AND b; -- legal (logical operation OK)

## Slide 23: Data types
There is a simple way of allowing data of type STD_LOGIC_VECTOR to participate directly in arithmetic operations
Using packages std_logic_signed or std_logic_unsigned
LIBRARY ieee;
USE ieee.std_logic_1164.all;
USE ieee.std_logic_unsigned.all; -- extra package included
...
SIGNAL a: STD_LOGIC_VECTOR (7 DOWNTO 0);
SIGNAL b: STD_LOGIC_VECTOR (7 DOWNTO 0);
SIGNAL x: STD_LOGIC_VECTOR (7 DOWNTO 0);
...
v <= a + b; -- legal (arithmetic operation OK), unsigned
w <= a AND b; -- legal (logical operation OK)

## Slide 24
Data Conversion

## Slide 25: Data Conversion (I)
VHDL does not allow direct operations (arithmetic, logical, etc.) between data of different types.
It is often necessary to convert data from one type to another.
If the data are closely related, then the std_logic_1164 of the ieee library provides straightforward conversion functions
TYPE long IS INTEGER RANGE -100 TO 100;
TYPE short IS INTEGER RANGE -10 TO 10;
SIGNAL x : short;
SIGNAL y : long;
...
y <= 2*x + 5; -- error, type mismatch
y <= long(2*x + 5); -- OK, result converted into type long

## Slide 26: Data Conversion (II)
Conversion using predefined functions
Data conversion functions can be found in the std_logic_arith package
  conv_integer(p) : Converts a parameter p of type INTEGER, UNSIGNED or SIGNED to an INTEGER value.
    Notice that STD_LOGIC_VECTOR is not included.
  conv_unsigned(p, b): Converts a parameter p of type INTEGER, UNSIGNED or SIGNED, to an UNSIGNED value with size b bits.
  conv_signed(p, b): Converts a parameter p of type INTEGER, UNSIGNED or SIGNED to a SIGNED value with size b bits.
  conv_std_logic_vector(p, b): Converts a parameter p of type INTEGER, UNSIGNED,or SIGNED to a STD_LOGIC_VECTOR value with size b bits.

## Slide 27: Data Conversion (III)
LIBRARY ieee;
USE ieee.std_logic_1164.all;
USE ieee.std_logic_arith.all;
...
SIGNAL a: IN UNSIGNED (7 DOWNTO 0);
SIGNAL b: IN UNSIGNED (7 DOWNTO 0);
SIGNAL y: OUT STD_LOGIC_VECTOR (7 DOWNTO 0);
...
y <= CONV_STD_LOGIC_VECTOR ((a+b), 8);
-- Legal operation: a+b is converted from UNSIGNED to an
-- 8-bit STD_LOGIC_VECTOR value, then assigned to y.
Example

## Slide 28: Check Yourself
Consider the following data types:
TYPE array1 IS ARRAY (7 DOWNTO 0) OF STD_LOGIC;
TYPE array2 IS ARRAY (3 DOWNTO 0, 7 DOWNTO 0) OF STD_LOGIC;
TYPE array3 IS ARRAY (3 DOWNTO 0) OF array1;
SIGNAL a : BIT;
SIGNAL b : STD_LOGIC;:
SIGNAL x : array1;
SIGNAL y : array2;
SIGNAL w : array3;
SIGNAL z : STD_LOGIC_VECTOR (7 DOWNTO 0);
Which statement of the red-rectangle is illegal and which is correct
a <= x(2);
b <= x(2);
b <= y(3,5);
b <= w(5)(3);
y(1)(0) <= z(7);
x(0) <= y(0,0);
x <= "1110000";
a <= "0000000";
y(1) <= x;
w(0) <= y;
w(1) <= (7=>'1', OTHERS=>'0');
y(1) <= (0=>'0', OTHERS=>'1');
w(2)(7 DOWNTO 0) <= x;
w(0)(7 DOWNTO 6) <= z(5 DOWNTO 4);
x(3) <= x(5 DOWNTO 5);
b <= x(5 DOWNTO 5);
y <= ((OTHERS=>'0'), (OTHERS=>'0'),
(OTHERS=>'0'), "10000001");
z(6) <= x(5);
z(6 DOWNTO 4) <= x(5 DOWNTO 3);
z(6 DOWNTO 4) <= y(5 DOWNTO 3);
y(6 DOWNTO 4) <= z(3 TO 5);
y(0, 7 DOWNTO 0) <= z;
w(2,2) <= '1';