## Slide 1: VHDL (Operators and Attributes)
Meisam Abdollahi
School of Computer Engineering
Iran University of Science and Technology
meisam.abdolahi@ut.ac.ir
Winter 1400 (Computer Aided Design)

## Slide 2: Outline
Concatenation
Aggregate
Alias
Operators
Attributes

## Slide 3: Concatenation
architecture EXAMPLE_1 of CONCATENATION is signal BYTE : bit_vector (7 downto 0); signal A_BUS, B_BUS : bit_vector (3 downto 0); begin BYTE <= A_BUS & B_BUS; end EXAMPLE;

## Slide 4: Aggregate (I)
A basic operation that combines one or more values into a composite value of a record or array type;
Aggregates are a grouping of values to form an array or record expression.
  Variable data_1 :Bit_vector(0 to 3) := (‘0’,’1’,’0’,’1’);
    Variable data_1 :Bit_vector(0 to 3) := (1=>‘1’,0=>’0’, 3=>’1’,2=>’0’);
  Signal data_Bus :std_logic_vector (15 downto 0)
    data_Bus<=(15 downto 8 => ‘0’, 7 downto 0 =>’1’);
  Signal data_Bus :std_logic_vector (15 downto 0)
    data_Bus<=(14 downto 8 => ‘0’, others=>’1’);
  Signal data_Bus :std_logic_vector (15 downto 0)
    data_Bus<=(others=>’z’);
  Type Status_record is record
    Code: Integer;
    Name: string(1 to 4);
  End record;
  Variable Status_var: Status_record :=(code=>57, name=>”MOVE”);

## Slide 5
signal Z_BUS : bit_vector (3 downto 0);
signal A_BIT, B_BIT, C_BIT, D_BIT : bit;
...
Z_BUS <= (A_BIT, B_BIT, C_BIT, D_BIT);
signal Z_BUS : bit_vector (3 downto 0);
signal A_BIT, B_BIT, C_BIT, D_BIT : bit;
...
Z_BUS <= ( 2=> B_BIT, 1 => C_BIT, 0 => D_BIT, 3 => A_BIT);
signal B_BIT : bit;
signal BYTE : bit_vector (7 downto 0);
...
BYTE<= (7 => '1', 5 downto 1 => '1', 6 => B_BIT, others => '0');
type T_PACKET is record
BYTE_ID : std_logic;
PARITY : std_logic;
ADDRESS : integer range 0 to 3;
DATA : std_logic_vector (3 downto 0);
end record
signal TX_DATA : T_PACKET;
...
TX_DATA <= ('1', '0', 2, "0101");
Aggregate (II)

## Slide 6
Alias

## Slide 7: Alias (I)
Aliases can significantly improve the readability of VHDL descriptions by using a shorthand notation for names
An alias is an alternative name for an existing object (signal, variable or constant). It does not define a new object.
Aliases allow reference to named items in different ways:
Example:
  Signal Instruction :Bit_vector(15 downto 0);
    Alias OpCode : Bit_vector(3 downto 0) is Instruction(15 downto 12);
    Alias Source : Bit_vector(1 downto 0) is Instruction(11 downto 10);
    Alias design : Bit_vector(1 downto 0) is Instruction(9 downto 8);
    Alias Immdata : Bit_vector(7 downto 0) is Instruction(7 downto 0);

## Slide 8: Alias (II)
alias SIGN : bit is DATA(31);
alias BYTE_ID : bit is NET_DATA_IN(7);
alias OPERAND : bit_vector(1 downto 0)
is CPU_BUFFER(LOW) (4 downto 3);
alias A : bit_vector(3 downto 0)
is CPU_BUFFER(HIGH)(3 downto 0);
alias B : bit_vector(2 downto 0)
is CPU_BUFFER(LOW) (2 downto 0);
signal BUS_A :
std_ulogic_vector(7 downto 0);
alias BIT_REV_A :
std_ulogic_vector(0 to 7) is BUS_A;

## Slide 9
Operators in VHDL

## Slide 10: Operators in VHDL
VHDL provides several kinds of pre-defined operators:
  Assignment operators
  Logical operators
  Arithmetic operators
  Relational operators
  Shift operators
  Concatenation operators

## Slide 11: Assignment Operators
<= Used to assign a value to a SIGNAL.
:= Used to assign a value to a VARIABLE, CONSTANT, or GENERIC.
  Used also for establishing initial values.
=> Used to assign values to individual vector elements or with OTHERS.
See an Example

## Slide 12: Assignment Operators (Example)
SIGNAL x : STD_LOGIC;
VARIABLE y : STD_LOGIC_VECTOR(3 DOWNTO 0); -- Leftmost bit is MSB
SIGNAL w: STD_LOGIC_VECTOR(0 TO 7); -- Rightmost bit is MSB
x <= '1'; -- '1' is assigned to SIGNAL x using "<=“
y := "0000"; -- "0000" is assigned to VARIABLE y using ":=“
w <= "10000000"; -- LSB is '1', the others are '0‘
w <= (0 =>'1', OTHERS =>'0'); -- LSB is '1', the others are '0'

## Slide 13: Logical Operators
Used to perform logical operations
The data must be of type BIT, STD_LOGIC
NOT
AND
OR
NAND
NOR
XOR
XNOR

## Slide 14: Logical Operators (Example)
y <= NOT a AND b; -- (a'.b)
y <= NOT (a AND b); -- (a.b)‘
y <= a NAND b; -- (a.b)'

## Slide 15: Arithmetic Operators
Used to perform arithmetic operations.
The data can be of type INTEGER, SIGNED, UNSIGNED, or REAL
+ Addition //no synthesis restrictions [binary operator]
- Subtraction //no synthesis restrictions [binary operator]
* Multiplication //no synthesis restrictions [binary operator]
/ Division //Only power of two dividers (shift operation) are allowed for synthesis [binary operator]
** Exponentiation //only constant values of base are accepted for synthesis. [binary operator]
MOD Modulus //y mod x returns the remainder of y/x with the signof x [binary operator] [Synthesizable when either y and x be constant or x be power of 2]
REM Remainder //y rem x returns the remainder of y/x with the signof y [binary operator] [Synthesizable when either y and x be constant or x be power of 2]
ABS Absolute value //returns the absolute value. With respect to the last three operators (mod, rem, abs), [unary operator]

## Slide 16: Arithmetic Operators (Examples)
variable A,B :Integer; variable C : Real; C:= 12.34 * ( 234.4 / 43.89 ); A:= B mod 2;
2 ** 8 = 256 3.8 ** 3 = 54.872 4 ** (-2) = 1 / (4**2) = 0.0625
signal INT1, INT2: integer := 0;
signal REAL1, REAL2: real := 6.7;
...
INT1 <= INT1 + 3;
REAL1 <= REAL2 - 2.2;
INT2 <= INT1 * REAL1; --illegal
INT2 <= INT1 * INTEGER(REAL1);
REAL2 <= REAL1 / 42.3;

## Slide 17: Difference between rem and mod in VHDL
mod & rem operate on integers & result is integer
rem has sign of 1st operand and is defined as: A rem B = A – (A/B) * B
mod has sign of 2nd operand and is defined as: A mod B = A – B * N -- for an integer N
  Note the absolute value of (A mod B) must be less than the absolute value of B.
5 rem 3 = 2
5 mod 3 = 2
(-5) rem 3 = -2 (-5) mod 3 = 1
(-5) rem (-3)= -2 (-5) mod (-3)= -2
5 rem (-3)= 2 5 mod (-3)= -1
7 mod 4 = 3
-7 mod 4 = 1
7 mod (-4) = –1
-7 mod (-4) = –3
-7 mod 4 = -7 -4*N  N can only
be -2 and mode be 1. The absolute of mod is less than 4.
Also mod has the sign
of second operand

## Slide 18: Comparison Operators
Used for making comparisons
The data can be of any of the types
= Equal to
/= Not equal to
< Less than
> Greater than
<= Less than or equal to
>= Greater than or equal to

## Slide 19: Shift Operators
Used for shifting data
  sll shift left logical (fill value is ‘0’)
  srl shift right logical (fill value is ‘0’)
  sla shift left arithmetic (fill value is right-hand bit)
  sra shift right arithmetic (fill value is left-hand bit)
  rol rotate left
  ror rotate right
All operators have two operands [ binary operator]:
  <left operand> <shift operation> <right operand>
  left operand is bit_vector to shift/rotate
  right operand is integer for # shifts/rotates
  - integer same as opposite operator with + integer

## Slide 20: Note
The VHDL arithmetic left shift operator is unusual. Instead of filling the LSB of the result with zero, it copies the original LSB into the new LSB. While this is an exact mirror image of the arithmetic right shift, it is not the conventional definition of the operator, and is not equivalent to multiplication by a power of 2.
In the VHDL 2008 standard this strange behavior was left unchanged (for backward compatibility) for argument types that do not have forced numeric interpretation (e.g., BIT_VECTOR) but 'SLA' for unsigned and signed argument types behaves in the expected way (i.e., rightmost positions are filled with zeros). VHDL's shift left logical (SLL) function does implement the aforementioned 'standard' arithmetic shift.

## Slide 21: Shift Operators (example)
“1100” sll 1 yields “1000”
“1100” srl 2 yields “0011”
“1100” sla 1 yields “1000”
“1100” sra 2 yields “1111”
“1100” rol 1 yields “1001”
“1100” ror 2 yields “0011”
“1100” ror –1 same as “1100” rol 1

## Slide 22: Check Yourself
SIGNAL a : BIT := '1';
SIGNAL b : BIT_VECTOR (3 DOWNTO 0) := "1100";
SIGNAL c : BIT_VECTOR (3 DOWNTO 0) := "0010";
SIGNAL d : BIT_VECTOR (7 DOWNTO 0);
x1 <= a & c; -> x1 <=
x2 <= c & b; -> x2 <=
x3 <= b XOR c; -> x3 <=
x4 <= a NOR b(3); -> x4 <=
x5 <= b sll 2; -> x5 <=
x6 <= b sla 2; -> x6 <=
x7 <= b rol 2; -> x7 <=
x8 <= a AND NOT b(0) AND NOT c(1); -> x8 <=
d <= (5=>'0', OTHERS=>'1'); -> d<=
“10010”
“11100”
“1110”
‘0’
“0000”
“0011”
“0011”
‘0’
“11011111”

## Slide 23
Attributes

## Slide 24: Attributes (I)
Language defined attributes return information about certain items in VHDL
  Types, subtypes
  Procedures, functions
  Signals, variables, constants
  Entities, architectures, configurations, packages
  Components
VHDL has several predefined attributes that are useful to the designer
Attributes can be user-defined to handle custom situations (user-defined records, etc.)

## Slide 25: Attributes (II)
Signal Attributes
  General form of attribute use is:
  Some examples of signal attributes
<name> ' <attribute_identifier>
X'EVENT -- evaluates TRUE when an event on signal X has just occurred.
X'LAST_VALUE -- Returns the value of X before the last event
X'STABLE -- evaluates TRUE when no event has occurred on signal X
X’ACTIVE -- Returns true if X = ‘1’
X’LAST_ACTIVE --Returns the time elapsed since last X = ‘1’
X’LAST_EVENT --Returns the time elapsed since last event
X’QUIET <time> --Returns true if no event has occurred during the time specified

## Slide 26: Attributes (III)
All four assignments shown below are synthesizable and equivalent
  IF (clk'EVENT AND clk='1')... -- EVENT attribute used with IF
  IF (NOT clk'STABLE AND clk='1')... -- STABLE attribute used with IF
  WAIT UNTIL (clk'EVENT AND clk='1'); -- EVENT attribute used with WAIT
  IF RISING_EDGE(clk)... -- call to a function

## Slide 27: Attributes (IV)
Value Attributes
'LEFT -- returns the leftmost value of a type
'RIGHT -- returns the rightmost value of a type
'HIGH -- returns the greatest value of a type
'LOW -- returns the lowest value of a type
'LENGTH -- returns the number of elements in a constrained array
'RANGE -- returns the range of an array
d’REVERSE_RANGE: Returns vector range in reverse order

## Slide 28: Attributes (V)
SIGNAL d : STD_LOGIC_VECTOR (7 DOWNTO 0);
d'LOW=0,
d'HIGH=7,
d'LEFT=7,
d'RIGHT=0,
d'LENGTH=8,
d'RANGE=(7 downto 0),
d'REVERSE_RANGE=(0 to 7).

## Slide 29: Attributes (Example)
SIGNAL x: STD_LOGIC_VECTOR (0 TO 7);
  Then all four LOOP statements below are synthesizable and equivalent
    FOR i IN RANGE (0 TO 7) LOOP ...
    FOR i IN x'RANGE LOOP ...
    FOR i IN RANGE (x'LOW TO x'HIGH) LOOP ...
    FOR i IN RANGE (0 TO x'LENGTH-1) LOOP ...

## Slide 30: Attributes (VI)
Example
TYPE count is RANGE 0 TO 127;
TYPE states is (idle, decision,read,write);
TYPE word is ARRAY(15 DOWNTO 0) of bit;
count'left = 0 states'left = idle word'left = 15
count'right = 127 states'right = write word'right = 0
count'high = 127 states'high = write word'high = 15
count'low = 0 states'low = idle word'low = 0
count'length = 128 states'length = 4 word'length = 16
count'range = 0 TO 127
word'range = 15 DOWNTO 0

## Slide 31: Check Yourself
c'LOW ->
d'HIGH ->
c'LEFT ->
d'RIGHT ->
c'RANGE ->
d'LENGTH ->
c'REVERSE_RANGE ->
SIGNAL a : BIT := '1';
SIGNAL b : BIT_VECTOR (3 DOWNTO 0) := "1100";
SIGNAL c : BIT_VECTOR (3 DOWNTO 0) := "0010";
SIGNAL d : BIT_VECTOR (7 DOWNTO 0);
0
7
3
0
3 DOWNTO 0
8
0 TO 3

## Slide 32: Check Yourself
Verify whether each of the operations below is legal or illegal. Briefly justify your answers.
b(0) AND a
a + d(7)
NOT b XNOR c
c + d
e - f
IF (b<c) ...
IF (b>=a) ...
IF (f/=e) ...
IF (e>d) ...
b sra 1
c srl -2
f ror 3
e*3
5**5
f/4
e/3
d <= c
d(6 DOWNTO 3) := b
e <= d
f := 100
SIGNAL a : BIT := '1';
SIGNAL b : BIT_VECTOR (3 DOWNTO 0) := "1100";
SIGNAL c : BIT_VECTOR (3 DOWNTO 0) := "0010";
SIGNAL d : BIT_VECTOR (7 DOWNTO 0);
SIGNAL e : INTEGER RANGE 0 TO 255;
SIGNAL f : INTEGER RANGE -128 TO 127;
--Legal
--illegal
--Legal
--illegal
--Legal
--Legal
--illegal
--Legal
--Legal
--Legal
--illegal
--illegal
--illegal
--illegal
--Legal
--Legal
--illegal
--Legal
--illegal
--Legal