## Slide 1: VHDL (Process)
Meisam Abdollahi
School of Computer Engineering
Iran University of Science and Technology
meisam.abdolahi@ut.ac.ir
Winter 1400 (Computer Aided Design)

## Slide 2: Outline
Concurrent and Sequential Statements
Process statement
Wait statement
Signals & variables in process
Global variables (Shared)
Postponed Process
If statements
Case statements
Loop statements
Clk generation
Flip-Flops
Synchron and Asynchron reset

## Slide 3: Concurrent and Sequential Statements
VHDL provides two different types of execution: sequential and concurrent
Different types of execution are useful for modeling of real hardware
Sequential statements view hardware from a programmer approach
Concurrent statements are order-independent and asynchronous

## Slide 4: Concurrent and Sequential Statements
Concurrent type such as: when-else, with-select, signal assignment, and etc.
Sequential type such as: if-then-else, case statement, loop statements, variable assignment, inside process and etc.,
Both sequential and concurrent such as: signal assignment, constants, function and procedure calls, after delay, and etc.
Important: codes inside process, function and procedures are sequential.
Important: codes inside architecture are concurrent

## Slide 5: Process Statement (I)
The process in VHDL is the mechanism by which sequential statements can be executed in the correct sequence.
Several processes execute concurrently
Processes in an architecture are executed concurrently with all other concurrent statements.
Execution is controlled either via sensitivity list (contains trigger signals), or wait-statements
The statements inside the process is executed whenever one or more elements of the sensitive list change value.

## Slide 6: Process Statement (II)
Process statements are executed concurrently but the statements inside a process are executed sequentially.
Every process is executed once upon initialization
A process statement has a declaration section and a statement part.
  In the declaration section, types, variables, constants, subprograms, and so on can be declared.
  The statement part contains only sequential statements.

## Slide 7: Process Definition
VARIABLES are optional. If used, they must be declared in the declarative part of the PROCESS
The initial value is not synthesizable, being only taken into consideration in simulations.
The use of a label is also optional. Its purpose is to improve code readability

## Slide 8: Process
JustToShow: process
Begin
Some statement 1;
Some statement 2;
Some statement 3;
Some statement 4;
wait<condition>;
end process JustToShow;
JustToShow: process
Begin
Some statement 1;
Some statement 2;
Some statement 3;
Some statement 4;
Some statement 5;
end process JustToShow;
Notes: 8

## Slide 9: Process
JustToShow: process ( )
Begin
Some statement 1;
Some statement 2;
Some statement 3;
Some statement 4;
end process JustToShow;
VHDL provides a construct called sensitivity list of a process
The list specified next to the process keyword.
The same as wait on sensitivity_list at the end of a process
JustToShow: process
Begin
Some statement 1;
Some statement 2;
Some statement 3;
Some statement 4;
wait on
end process JustToShow;
SomeSig

## Slide 10: Process
JustToShow: process (signa1,signal2,signal3)
Begin
Some statement 1;
Some statement 2;
Some statement 3;
Some statement 4;
Some statement 5;
end process JustToShow;
Signal2 has changed
Signal3 has changed
Sensitive list

## Slide 11: Process: an example
ARCHITECTURE archlist OF list IS
BEGIN
nand_test: PROCESS (a,b)
BEGIN
c <= NOT (a AND b);
END PROCESS nand_test;
END archlist;
a
b
c
the process ‘nand’ is sensitive to signals ‘a’ and ‘b’ i.e., whenever signal ‘a’ or ‘b’ changes value, the statements inside of the process will be evaluated

## Slide 12: Wait Statement
A process may be suspended upon execution of a wait statement in the process. The process remains suspended until its reactivation condition is met
Three kind of reactivation condition can be specified in a wait statement
Conditions can be mixed. e.g
  wait on A, B until Enable = 1;
It is illegal to use wait statement in a process with a sensitivity list
  timeout wait for time-expression; //simulation only
  condition wait until condition; //Synthesizable
  signal sensitivity wait on signal-list; //Synthesizable

## Slide 13: Wait Until
WAIT UNTIL signal_condition;
  The WAIT UNTIL statement accepts only one signal
  More appropriate for synchronous code than asynchronous
  WAIT UNTIL must be the first statement in the PROCESS
  The PROCESS will be executed every time the condition is met.

## Slide 14: Wait Until (Example)
PROCESS -- no sensitivity list
BEGIN
WAIT UNTIL (clk'EVENT AND clk='1');
IF (rst='1') THEN
output <= "00000000";
ELSIF (clk'EVENT AND clk='1') THEN
output <= input;
END IF;
END PROCESS;

## Slide 15: WAIT ON
WAIT ON signal1 [, signal2, ... ];
  WAIT ON accepts multiple signals
  The PROCESS is put on hold until any of the signals listed changes
PROCESS
BEGIN
WAIT ON clk, rst;
IF (rst='1') THEN
output <= "00000000";
ELSIF (clk'EVENT AND clk='1') THEN
output <= input;
END IF;
END PROCESS;

## Slide 16: Wait: an Example
  Or_process : process (In1, In2)
  begin
  Output <= In1 or In2;
  end process;
  Or_process : process
  Begin
  wait on In1, In2;
  Output <= In1 or In2;
  end process;
Wait for type expression
Wait until condition
Wait on sensitivity list
Complex wait
Wait for 10ns (simulation)
Wait until CLK=‘1’
Wait on Enable
Wait unit date after 10ns
(simulation)

## Slide 17
Variables vs. Signals in process

## Slide 18: Variables vs. signals in process
Variables and signals show a fundamentally different behavior.
In a process, the last signal assignment to a signal is carried out when the process execution is suspended.
Value assignments to variables, however, are carried out immediately.

## Slide 19: Signals and Processes
Goal: the difference between how a signal assignment and variable assignment behave in the process statement.
...
signal x,y,z : bit;
...
process (y)
begin
x<=y;
z<=not x;
end process;
If the signal y changes then an event will be scheduled on x to make it the same as y.
An event is scheduled on z to make it the opposite of x.
Question: will the value of z be the opposite of y?
The answer is NO, because when the second statement is executed, the event on x has not been processed yet, and the event scheduled on z will be the opposite of the value of x

## Slide 20: Variables and Processes
process (y)
variable x,z : bit;
begin
x:=y;
z:=not x;
end process;
The value of the variable z would be the opposite of the value of y because the value of the variable x is changed immediately.
Variables are only available within processes:
  Name within process declarations
  Known only in this process
Possible assignments:
  Signal to variable
  Variable to signal
  Types have to match

## Slide 21: Variables in process
architecture RTL of XYZ is
signal A, B, C : integer range 0 to 7;
signal Y, Z : integer range 0 to 15;
begin
process (A, B, C)
variable M, N : integer range 0 to 7;
begin
M := A;
N := B;
Z <= M + N;
M := C;
Y <= M + N;
end process;
end RTL;

## Slide 22: Variables vs. signals in process
signal A,B,C: integer;
signal Y, Z : integer;
begin
process (A,B,C)
variable M, N:
integer;
begin
M := A;
N := B;
Z <= M + N;
M := C;
Y <= M + N;
end process;
signal A,B,C: integer;
signal Y, Z : integer;
signal M, N : integer;
begin
process (A,B,C,M,N)
begin
M <= A;
N <= B;
Z <= M + N;
M <= C;
Y <= M + N;
end process;

## Slide 23: Variables vs. signals in process (II)
Signal values are assigned after the process execution
Only the last signal assignment is carried out
M ⇐ A; is overwritten by M ⇐ C;
The 2nd adder input is connected to C

## Slide 24: Exam question (Check Yourself)
What is the value of sum in the following two pieces of code? Please determine the value of sum for the first 4 clocks
entity mysig is
port(clk: in bit; sum: out integer range 0 to 256);
end mysig;
architecture beh of mysig is
signal sig1: integer :=1;
signal sig2: integer :=2;
signal sig3: integer :=3;
begin
process(clk)
begin
if(clk'event and clk='1') then
sig1 <=sig2 + sig3;
sig2 <= sig1;
sig3 <=sig2;
sum<=sig1 + sig2 + sig3;
end if;
end process;
end architecture;
entity myvar is
port(clk: in bit; sum: out integer range 0 to 256);
end myvar;
architecture beh of myvar is
begin
process(clk)
variable var1: integer :=1;
variable var2: integer :=2;
variable var3: integer :=3;
begin
if(clk'event and clk='1') then
var1:=var2 + var3;
var2 := var1;
var3 :=var2;
sum<=var1 + var2 + var3;
end if;
end process;
end architecture;

## Slide 25: Exam Question: Solution I
In myvar program:
In clock 1:
Var1 = 2+3 = 5
Var2 = 5
Var3 = 5  sum = 5 + 5 + 5  sum = 15
In clock 2:
Var1 = 5 + 5 = 10
Var2 = 10
Var3 = 10  sum = 10 + 10 + 10  sum =30;
In clock3:
Var1 = 10 + 10 = 20
Var2 = 20
Var3 = 20  sum 20 + 20 + 20  sum = 60
In clock4:
Var1 = 20 + 20 = 40
Var2 = 40
Var3 = 40  sum = 40 + 40 + 40  sum = 120

## Slide 26: Exam Question: Solution II
In mysig program:
In clock1:
All signal assignments are taken at the beginning of clock 2; thereby in clock 1 you have
Sig1 = 1
Sig2 = 2
Sig3 = 3  sum = 1+2+3  sum = 6
In clock2:
Now, the signal assignments of clock 1 are taken here; while the signal assignments of clock 2 are taken at the beginning of clock 3. So, we have
Sig1 = 2 + 3 = 5
Sig2 = 1 (the value of signal sig1 of clock 1)
Sig3 = 2 (the value of sig2 of clock 1)  sum = 5 + 1 + 2 = 8
In clock3:
Now, the signal assignments of clock 2 are taken here; while the signal assignments of clock 3 are taken at the beginning of clock 4. So, we have
Sig1 = 1 + 2 = 3
Sig2 = 5 (the value of signal sig1 of clock 2)
Sig3 = 1 (the value of sig2 of clock 2)  sum = 3 + 5 + 1  sum = 9
In clock4:
Now, the signal assignments of clock 3 are taken here; while the signal assignments of clock 4 are taken at the beginning of clock 5. So, we have
Sig1 = 5 + 1 = 6
Sig2 = 3 (the value of signal sig1 of clock 3)
Sig3 = 5 (the value of sig2 of clock 3)  sum = 6 + 3 + 5  sum = 14

## Slide 27
Global Variables (Shared)

## Slide 28: Global Variables
In VHDL 93, global variables are allowed.
These variables are not only visible within a process but within the entire architecture.
The problem may occur, that two processes assign a different value to a global variable at the same time. It is not clear then, which of these processes assigns the value to the variable last.
  This can lead to a non-deterministic behavior!
In synthesizable VHDL code global variables must not be used.

## Slide 29: Global Variables (II)
architecture BEHAVE of SHARED is shared variable S : integer; begin process (A, B) begin S := A + B; end process; process (A, B) begin S := A - B; end process; end BEHAVE; | Accessible by all processes of an architecture (shared variables) Can introduce non-determinism
Not to be used in synthesizable code | 

## Slide 30
Postponed Process

## Slide 31: Postponed Process (I)
Ex: Process (a, b, c)
Begin
. . .
End Process;
IF a, b, c Change in Zero-Time but with one d-Delay from one another 
  Multiple Process Activation (within d-Delay of Each other)
  The final Activation Signal Transactions will Dominate
  Unnecessary Execution of Processes result in Slower Operation
Postponed Processes Activate Only After All Sensitivity List Signals Stabilize.
Activates 3 Times Once Per Sensitivity List Signal Change

## Slide 32: Postponed Process (II)
Ex: Postponed Process (a, b, c)
Begin
. . . . . .
End Process;
Concurrent Statements, e.g. Signal Assignment, Are Also Sensitive to Changes in Signals on Their Right Hand Side  Postponed Keyword Can Be Used in This Case As Well.
Example
Concurrent1: Postponed a <= b AND c OR d ;
Activates Only After All Sensitivity List Signals Stabilize (c in this case).

## Slide 33
If Statement

## Slide 34: If Statement
The general form is
    if condition1 then
    statement1
    elsif condition2 then
    statement2
    else
    statement3
    end if;

## Slide 35: If Example: Two-input NAND gate
LIBRARY IEEE;
USE IEEE.std_logic_1164.ALL;
ENTITY mynand2 is
PORT( a, b : IN std_logic;
c : OUT std_logic);
END entity;
ARCHITECTURE mynand OF mynand2 IS
BEGIN
PROCESS( a, b )
VARIABLE temp : std_logic;
BEGIN
temp := NOT (a and b);
IF (temp = '1') THEN
c <= temp AFTER 6 ns;
ELSIF (temp = '0') THEN
c <= temp AFTER 5 ns;
ELSE
c <= temp AFTER 6 ns;
END IF;
END PROCESS;
END architecture;
Declares a VHDL package that provides the necessary information with 9 state logic.
The architecture contains only one statement, a concurrent process statement.
The process declaration section declares a local variable named temp.
The process statement part has two sequential statements in it
explicit sensitivity list

## Slide 36: If: an Example
library ieee;
use ieee.std_logic_1164.all;
entity myand is
port(in1, in2: in std_logic;
out1: out std_logic);
end entity;
architecture myand of myand is
constant Delay: time:= 5 ns;
begin
And_process : process (in1, in2)
begin
if In1 = '0' or In2 = '0' then
Out1 <= '0' after Delay;
elsif In1 = 'X' or In2 = 'X' then
Out1 <= 'X' after Delay;
else
Out1 <= '1' after Delay;
end if;
end process;
end architecture;
The name of the architecture is the same name as the entity name. This is legal
Logical or for checking a condition. It is not a gate!
In an if statement, using parenthesis is optional

## Slide 37: If: an Example
process
begin
if (reset = ‘1’) then
A <= ‘0’ ;
elsif (clk’event and clk = ‘1’) then
A <= ‘B’;
end if;
wait on reset, clk;
end process;
process (clk,reset)
begin
if (reset = ‘1’) then
A <= ‘0’;
elsif (clk’event and clk = ‘1’) then
A <= ‘B’;
end if;
end process;

## Slide 38: If: an Example
IF (x<y) THEN temp:="11111111";
ELSIF (x=y AND w='0') THEN temp:="11110000";
ELSE temp:=(OTHERS =>'0');
End if;

## Slide 39: One-digit Counter
LIBRARY ieee;
USE ieee.std_logic_1164.all;
---------------------------------------------
ENTITY counter IS
PORT (clk : IN STD_LOGIC;
digit : OUT INTEGER RANGE 0 TO 9);
END counter;
---------------------------------------------
ARCHITECTURE counter OF counter IS
BEGIN
count: PROCESS(clk)
VARIABLE temp : INTEGER RANGE 0 TO 10;
BEGIN
IF (clk'EVENT AND clk='1') THEN
temp := temp + 1;
IF (temp=10) THEN temp := 0;
END IF;
END IF;
digit <= temp;
END PROCESS count;
END counter;

## Slide 40
Case Statements

## Slide 41: Case Statement
Syntax
  case expression is
  when choice 1 =>
  statement_A;
  when choice 3 to 5 =>
  statement_B;
  when choice 8 downto 6 =>
  statement_C;
  when choice 9 | 13 | 17 =>
  statement_D;
  when others =>
  statement_E;
  end case;

## Slide 42: Case Statement: an Example
MUX (41)
  mycase_pro: process (s, c, d, e, f)
  begin
  case s is
  when "00" =>
  pout <= c;
  when "01" =>
  pout <= d;
  when "10" =>
  pout <= e;
  when others =>
  pout <= f;
  end case;
  end process mycase_pro;
C
D
E
F
S
POUT

## Slide 43: Case Statement
CASE allows multiple assignments for each test condition
WHEN value -- single value
WHEN value1 To value2 -- range, for enumerated data types only
WHEN value1 | value2 |... -- value1 or value2 or ...

## Slide 44: Null
Nothing to do
Equivalent to No Operation
It can be used by case statement
  process (count)
  begin
  case count is
  when 0 =>
  dout <= “00”;
  when 1 to 15 =>
  dout <= “01”;
  when 16 to 255 =>
  dout <= “10”;
  when others =>
  null;
  end case;
  end process;

## Slide 45
Loops

## Slide 46: Loop (I)
The LOOP statement is used whenever an operation needs to be repeated.
The LOOP statement has an optional label, which can be used to identify the LOOP statement.
VHDL provides three kinds of Loop statements
  Simple loop
  for loop
  while loop

## Slide 47: Simple Loop
Simple loop
  Simple loop encloses a set of statements in a structure which is set to loop forever
  The general form is
    label1 : loop
    statements
    end loop label1;

## Slide 48: Simple Loop: Example
library ieee;
use ieee.std_logic_1164.all;
entity WhileTest is
port(A: in integer range 0 to 31;
Z: out std_logic_vector(3 downto 0));
end entity;
architecture test of WhileTest is
begin
process (A)
variable I : integer range 0 to 4;
begin
Z <= "0000";
I := 0;
L1: loop
exit L1 when I = 4;
if (A = I) then
Z(I) <= '1';
end if;
I := I + 1;
end loop;
end process;
Note VHDL allows maximum 10000 iterations.

## Slide 49: For Loop (I)
The FOR loop loops as many times as specified in the discrete_range, unless the loop is exited
The general form
  loop_label: -- optional
  for loop_variable in range loop
  statements
  end loop loop_label;
Example

## Slide 50: For Loop Example
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;
entity LoopTest is
port(A: in std_logic_vector(1 downto 0);
Z: out std_logic_vector(3 downto 0));
end entity;
architecture LoopTest of LoopTest is
signal t: integer;
begin
t<= to_integer(unsigned(A));
process(A)
begin
Z<="0000";
for i in 0 to 3 loop
if i=t then
Z(i)<='1';
end if;
end loop;
end process;
end architecture;
Package for converting std_logic to integer

## Slide 51: For Loop (II)
In some languages, the loop index (in this example, i) can be assigned a value inside the loop to change its value.
VHDL does not allow any assignment to the loop index.
The index value i is locally declared by the FOR statement.
  The variable i does not need to be declared explicitly in the process, function, or procedure
If another variable of the same name exists in the process, then these two variables are treated as separate variables

## Slide 52: For Loop (III)
PROCESS(i)
BEGIN
x <= i + 1; -- x is a signal
FOR i IN 1 to a/2 LOOP
q(i) := a; -- q is a variable
END LOOP;
END PROCESS;
The index value i is not the same object as the signal i that was used to calculate the new value for signal x.
Inside the FOR loop, when a reference is made to i, the local index is retrieved.
But outside the FOR loop, when a reference is made to i, the value of the signal i in the sensitivity list of the process is retrieved.

## Slide 53: For Loop (IV)
The values used to specify the range in the FOR loop need not be specific integer values.
The range can be any discrete range.
See Examples

## Slide 54: For Loop (V)
PROCESS(clk)
TYPE day_of_week IS (sun, mon, tue, wed, thur, fri, sat);
BEGIN
FOR i IN day_of_week LOOP
IF i = sat THEN
son <= mow_lawn;
ELSIF i = sun THEN
church <= family;
ELSE
dad <= go_to_work;
  END IF;
END LOOP;
END PROCESS;
The range is specified by the type.
Here, the compiler determines that the leftmost value is sun, and the rightmost value is sat.
The range then is determined as from
sun to sat.

## Slide 55: For Loop (VI)
If an ascending range is desired, use the to clause. The downto clause can be used to create a descending range.
See Example
PROCESS(x, y)
BEGIN
FOR i IN x downto y LOOP
q(i) := w(i);
END LOOP;
END PROCESS;

## Slide 56
While Loop

## Slide 57: While Loop (I)
The WHILE condition LOOP statement loops as long as the condition expression is TRUE.
The general form:
  loop_label:
  while condition loop
  statements
  end loop loop_label;
See Example

## Slide 58: While Loop (II)
library ieee;
use ieee.std_logic_1164.all;
entity WhileTest is
port(A: in integer range 0 to 3;
Z: out std_logic_vector(3 downto 0));
end entity;
architecture test of WhileTest is
begin
process (A)
variable I :
integer range 0 to 4;
begin
Z <= "0000";
I := 0;
while (I <= 3) loop
if (A = I) then
Z(I) <= '1';
end if;
I := I + 1;
end loop;
end process;
end architecture;

## Slide 59: Exit and Next statement
Exit statement is a sequential statement closely associated with loops and causes the loop to be exited
    for i in 0 to 7 loop
    if ( i = 4 ) then
    exit;
    end if;
    end loop;
Next statement is used to advance control to the next iteration of the loop
    for i in 0 to 7 loop
    if ( i = 4 ) then
    next;
    end if;
    end loop;

## Slide 60: Nested Loop
process
begin
for i in 0 to 3 loop
for j in 0 to 3 loop
wait for 10 ns;
b <= b + 1;
end loop;
a <= a + 1;
end loop;
wait;
end process;

## Slide 61
Generate Positive Edge of Clock

## Slide 62: CLK Generation
The most popular clk generation
Process (clk)
Begin
if( clk’event and clk=‘1’) then
….
end if;
end process;
Process (clk)
Begin
if( clk=‘1’) then
….
end if;
end process;
Process (clk)
Begin
if( clk’event and clk=‘1’ and clk’last_value=‘0’) then
….
end if;
end process;
Process (clk)
Begin
wait until clk=‘1’;
….
end process;
Selection depends on synthesis tools

## Slide 63: D-Flip Flop
  library IEEE;
  use IEEE.std_logic_1164.all;
  entity d_ff is
  port (data, clk : in std_logic;
  q : out std_logic);
  end d_ff;
  architecture behav of d_ff is
  begin
  process (clk) begin
  if (clk'event and clk = '1') then
  q <= data;
  end if;
  end process;
  end behav;

## Slide 64: D-Flip Flop with Asynchronous Reset
  library IEEE;
  use IEEE.std_logic_1164.all;
  entity d_ff is
  port (data, clk,reset : in std_logic;
  q : out std_logic);
  end d_ff;
  architecture behav of d_ff is
  begin
  process (clk, reset) begin
  if reset=‘1’ then
  q<=‘0’;
  elsif (clk'event and clk = '1') then
  q <= data;
  end if;
  end process;
  end behav;
reset

## Slide 65: D-Flip Flop with Synchronous Reset
  library IEEE;
  use IEEE.std_logic_1164.all;
  entity d_ff is
  port (data, clk,reset : in std_logic;
  q : out std_logic);
  end d_ff;
  architecture behav of d_ff is
  begin
  process (clk, reset) begin
  if( clk’event and clk=‘1’) then
  if reset=‘1’ then
  q<=‘0’;
  elsif
  q <= data;
  end if;
  end if;
  end process;
  end behav;
reset

## Slide 66
Using Sequential Code to Design Combinational Circuits

## Slide 67: Using Sequential Code to Design Combinational Circuits
Sequential code can be used to implement either sequential or combinational circuits.
To design a combinational circuit, the following rules should be observed
  Rule 1: Make sure that all input signals used (read) in the PROCESS appear in its sensitivity list.
  Rule 2: Make sure that all combinations of the input/output signals are included in the code;

## Slide 68: Example
ENTITY example IS
PORT (a, b, c, d: IN STD_LOGIC;
sel: IN INTEGER RANGE 0 TO 3;
x, y: OUT STD_LOGIC);
END example;
ARCHITECTURE example OF example IS
BEGIN
PROCESS (a, b, c, d, sel)
BEGIN
IF (sel=0) THEN
x<=a;
y<='0';
ELSIF (sel=1) THEN
x<=b;
y<='1';
ELSIF (sel=2) THEN
x<=c;
ELSE
x<=d;
END IF;
END PROCESS;
END example;