## Slide 1: VHDL (State Machine)
Meisam Abdollahi
School of Computer Engineering
Iran University of Science and Technology
meisam.abdolahi@ut.ac.ir
Winter 1400 (Computer Aided Design)

## Slide 2: Outline
Structure of a Digital System
State Machines
  Moore Machine
  Mealy Machine
Moore Machine in VHDL
Mealy Machine in VHDL
How to Design Optimum State Machines

## Slide 3
Structure of Digital Systems

## Slide 4: Structure of a Typical Digital System
Datapath
(Execution
Unit)
Controller
(Control
Unit)
Data Inputs
Data Outputs
Control Inputs
Control Outputs
Control
Signals
Status
Signals

## Slide 5: Datapath (Execution Unit)
Manipulates and processes data
Performs arithmetic and logic operations, shifting, and other data-processing tasks
Composed of registers, gates, multiplexers, decoders, adders, comparators, ALUs, etc.
Provides all necessary resources and interconnects among them to perform specified task
Interprets control signals from the Controller and generates status signals for the Controller

## Slide 6: Controller (Control Unit)
A controller controls data movements in the datapath by switching multiplexers and enabling or disabling resources
    Example: enable signals for Registers
    Example: control signals for Muxes
Provides signals to activate various processing tasks in the Datapath
Determines the sequence of the operations performed by Datapath

## Slide 7: Controller
Controller can be programmable or non-programmable
Programmable
  Has a program counter which points to the next instruction
  Instructions are held in a RAM or ROM externally
  Micro-programming is an example of programmable controller
Non-Programmable
  It is a “hardwired state machine” or “hardwired instructions”
  We will be focusing primarily on the non-programmable type in this course

## Slide 8
Finite State Machine

## Slide 9: Finite State Machines (I)
Digital Systems and especially their Controllers can be described as Finite State Machines (FSMs)
Finite State Machines can be represented using
  State Diagrams and State Tables - suitable for simple digital systems with a relatively few inputs and outputs
  Algorithmic State Machine (ASM) Charts - suitable for complex digital systems with a large number of inputs and outputs

## Slide 10: Finite State Machines (II)
Any Circuit with Memory is a Finite State Machine
  Even computers can be viewed as huge FSMs
Design of FSMs involves
  Defining states
  Defining transitions between states
  Determining the output
  Optimization / minimization
Manual Optimization/Minimization is Practical for Small FSMs Only

## Slide 11: Moore FSM
Output is a Function of a Present State Only
Inputs
Next State
function
Present
State register
Output
function
Outputs
clock
reset
Current state

## Slide 12: Mealy FSM
Output Is a Function of a Present State and Inputs
Inputs
Next State
function
Present
State register
Output
function
Outputs
clock
reset
Current state

## Slide 13: Moore Machine
state 1
output 1
state 2
output 2
transition
condition 1
transition
condition 2

## Slide 14: Mealy Machine
state 1
state 2
transition condition 1
output 1
transition condition 2
output 2

## Slide 15: Moore vs. Mealy FSM (I)
Moore and Mealy FSMs Can Be Functionally Equivalent
  Equivalent Mealy FSM can be derived from Moore FSM and vice versa
Mealy FSM Has Richer Description and Usually Requires Smaller Number of States
  Smaller circuit area

## Slide 16: Moore vs. Mealy FSM (II)
Mealy FSM Computes Outputs as soon as Inputs Change
  Mealy FSM responds one clock cycle sooner than equivalent Moore FSM
Moore machine is synchronize with clock, but Mealy machine is not

## Slide 17: Moore FSM - Example 1
Moore FSM that Recognizes Sequence “10”
S0/0
S1/0
S2/1
0
0
0
1
1
1
reset
Meaning
of states:
S0: No
elements
of the
sequence
observed
S1: “1”
observed
S2: “10”
observed

## Slide 18: Mealy FSM - Example 1
Mealy FSM that Recognizes Sequence “10”
S0
S1
0 / 0
1 / 0
1 / 0
0 / 1
reset
Meaning
of states:
S0: No
elements
of the
sequence
observed
S1: “1”
observed

## Slide 19: Moore & Mealy FSMs – Example 1
clock
input
Moore
Mealy
0 1 0 0 0
S0 S1 S2 S0 S0
S0 S1 S0 S0 S0

## Slide 20
Finite State Machines
in VHDL

## Slide 21: FSMs in VHDL
Finite State Machines can be easily described with processes
Synthesis Tools understand FSM description if certain rules are followed:
  State transitions should be described in a process sensitive to clock and reset signals
  Outputs described as concurrent statements outside the process

## Slide 22: Moore FSM in VHDL
Inputs
Next State
function
Present State register
Output
function
Outputs
clock
reset
Current state
process(clock, reset)
concurrent
statements

## Slide 23: Moore FSM - Example (I)
Moore FSM that Recognizes Sequence “10”
S0/0
S1/0
S2/1
0
0
0
1
1
1
reset

## Slide 24: Moore Example (II)
LIBRARY ieee;
USE ieee.std_logic_1164.ALL;
ENTITY sequencer is
PORT(clk, reset, input : IN std_logic;
output: OUT std_logic);
End ENTITY;
Architecture moore of sequencer is
TYPE state iS (S0, S1, S2); -- state declaration
SIGNAL Moore_state: state;
BEGIN
U_Moore: PROCESS (clk, reset)
begin
IF (reset = ‘1’) THEN
Moore_state <= S0;
ELSIF (clk’event AND clk=‘1’) THEN
CASE Moore_state IS
WHEN S0 =>
IF input = ‘1’ THEN
Moore_state <= S1;
ELSE
Moore_state <= S0;
END IF;

## Slide 25: Moore Example (III)
WHEN S1 =>
IF input = ‘0’ THEN
Moore_state <= S2;
ELSE
Moore_state <= S1;
END IF;
WHEN S2 =>
IF input = ‘0’ THEN
Moore_state <= S0;
ELSE
Moore_state <= S1;
END IF;
END CASE;
END IF;
END PROCESS;
Output <= ‘1’ WHEN Moore_state = S2 ELSE ‘0’;
END Architecture;
Output: concurrent statements

## Slide 26: Mealy FSM in VHDL
Output is a Function of a Present State and Inputs
Inputs
Next State
function
Present State register
Output
function
Outputs
clock
reset
Current state
process(clock, reset)
concurrent
statements

## Slide 27: Mealy FSM - Example (I)
Mealy FSM that Recognizes Sequence “10”
S0
S1
0 / 0
1 / 0
1 / 0
0 / 1
reset

## Slide 28: Mealy Example (II)
LIBRARY ieee;
USE ieee.std_logic_1164.ALL;
ENTITY sequencer is
PORT(clk, reset, input : IN std_logic;
output: OUT std_logic);
End ENTITY;
Architecture Mealy of sequencer is
TYPE state IS (S0, S1);
SIGNAL Mealy_state: state;
BEGIN
U_Mealy: PROCESS(clk, reset)
BEGIN
IF(clk’event AND clk = ‘1’) THEN
IF reset=‘1’ THEN
Mealy_state <= S0;
ELSE
CASE Mealy_state IS
WHEN S0 =>
IF input = ‘1’ THEN
Mealy_state <= S1;
ELSE
Mealy_state <= S0;
END IF;

## Slide 29: Mealy Example (III)
WHEN S1 =>
IF input = ‘0’ THEN
Mealy_state <= S0;
ELSE
Mealy_state <= S1;
END IF;
END CASE;
END IF;
END IF;
END PROCESS;
Output <= ‘1’ WHEN (Mealy_state = S1 AND input = ‘0’) ELSE ‘0’;
END Architecture;

## Slide 30
C
z
1
=
/
resetn
B
z
0
=
/
A
z
0
=
/
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=
Moore FSM - Example (II)

## Slide 31
Present
Next state
Output
state
w
=
0
w
=
1
z
A
A
B
0
B
A
C
0
C
A
C
1
Moore FSM – State table

## Slide 32: Moore FSM Example 2: VHDL code (I)
Library ieee;
USE ieee.std_logic_1164.all ;
ENTITY simple IS
PORT ( clock : IN STD_LOGIC ;
resetn : IN STD_LOGIC ;
w : IN STD_LOGIC ;
z : OUT STD_LOGIC ) ;
END simple ;
ARCHITECTURE Behavior OF simple IS
TYPE State_type IS (A, B, C) ;
SIGNAL y : State_type ;
BEGIN
PROCESS ( resetn, clock )
BEGIN
IF resetn = '0' THEN
y <= A ;
ELSIF (Clock'EVENT AND Clock = '1') THEN

## Slide 33: Moore FSM Example 2: VHDL code (II)
CASE y IS
WHEN A =>
IF w = '0' THEN
y <= A ;
ELSE
y <= B ;
END IF ;
WHEN B =>
IF w = '0' THEN
y <= A ;
ELSE
y <= C ;
END IF ;
WHEN C =>
IF w = '0' THEN
y <= A ;
ELSE
y <= C ;
END IF ;
END CASE ;

## Slide 34: Moore FSM Example 2: VHDL code (III)
END IF ;
END PROCESS ;
z <= '1' WHEN y = C ELSE '0' ;
END Behavior ;

## Slide 35
A
w
0
=
z
0
=
/
w
1
=
z
1
=
/
B
w
0
=
z
0
=
/
resetn
w
1
=
z
0
=
/
Mealy FSM - Example (II)

## Slide 36
Present
Next state
Output
z
state
w
=
0
w
=
1
w
=
0
w
=
1
A
A
B
0
0
B
A
B
0
1
Mealy FSM – State table

## Slide 37: Mealy FSM Example 2: VHDL code
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY Mealy IS
PORT ( clock : IN STD_LOGIC ;
resetn : IN STD_LOGIC ;
w : IN STD_LOGIC ;
z : OUT STD_LOGIC ) ;
END Mealy ;
ARCHITECTURE Behavior OF Mealy IS
TYPE State_type IS (A, B) ;
SIGNAL y : State_type ;
BEGIN
PROCESS ( resetn, clock )
BEGIN
IF resetn = '0' THEN
y <= A ;
ELSIF (clock'EVENT AND clock = '1') THEN

## Slide 38: Mealy FSM Example 2: VHDL code
CASE y IS
WHEN A =>
IF w = '0' THEN
y <= A ;
ELSE
y <= B ;
END IF ;
WHEN B =>
IF w = '0' THEN
y <= A ;
ELSE
y <= B ;
END IF ;
END CASE ;
END IF ;
END PROCESS ;
WITH y SELECT
z <= w WHEN B,
‘0’ WHEN others;
END Behavior ;

## Slide 39: Design an Optimum State Machine
Select the state machine depends on type and constrains of design
  Time schedule
  Area
  Speed
  Outputs without wavelet
Use a combination of Mealy and Moore

## Slide 40: Outline
Design Style #1
BCD Counter
Design Style #2 (Stored Output)
String Detector
Traffic Light Controller (TLC)

## Slide 41
Design Style #1

## Slide 42: Mealy state machine diagram
The separation of the circuit into two sections allows the design to be broken into two parts:
  The lower part, being sequential, will require a PROCESS,
  While the upper part, being combinational, will not
The sequential code can implement both types of logic, combinational as well as sequential.
If desired, the upper part can also be implemented using a PROCESS.

## Slide 43: Design of the Lower (Sequential) Section
PROCESS (reset, clock)
BEGIN
IF (reset='1') THEN
pr_state <= state0;
ELSIF (clock'EVENT AND clock='1') THEN
pr_state <= nx_state;
END IF;
END PROCESS;
It consists of an asynchronous reset, which determines the initial state of the system (state0),
The synchronous storage of nx_state (at the positive transition of clock)
One good thing about this approach is that the design of the lower section is basically standard.
Another advantage of this design style is that the number of registers is minimum.

## Slide 44: Design of the Upper (Combinational) Section
PROCESS (input, pr_state)
BEGIN
CASE pr_state IS
WHEN state0 =>
IF (input = ...) THEN
output <= <value>;
nx_state <= state1;
ELSE ...
END IF;
WHEN state1 =>
IF (input = ...) THEN
output <= <value>;
nx_state <= state2;
ELSE ...
END IF;
WHEN state2 =>
IF (input = ...) THEN
output <= <value>;
nx_state <= state2;
ELSE ...
END IF;
...
END CASE;
END PROCESS;
It does two things:
it assigns the output value and
it establishes the next state.
Note that all input signals are present in the sensitivity list and all input/output combinations are specified

## Slide 45: State Machine Template for Design Style #1
LIBRARY ieee;
USE ieee.std_logic_1164.all;
-----------------------------------------------------
ENTITY <entity_name> IS
PORT ( input: IN <data_type>;
reset, clock: IN STD_LOGIC;
output: OUT <data_type>);
END <entity_name>;
-----------------------------------------------------
ARCHITECTURE <arch_name> OF <entity_name> IS
TYPE state IS (state0, state1, state2, state3, ...);
SIGNAL pr_state, nx_state: state;
BEGIN
---------- Lower section: ------------------------
PROCESS (reset, clock)
BEGIN
IF (reset='1') THEN
pr_state <= state0;
ELSIF (clock'EVENT AND clock='1') THEN
pr_state <= nx_state;
END IF;
END PROCESS;
---------- Upper section: ------------------------
PROCESS (input, pr_state)
BEGIN
CASE pr_state IS
WHEN state0 =>
IF (input = ...) THEN
output <= <value>;
nx_state <= state1;
ELSE ...
END IF;
WHEN state1 =>
IF (input = ...) THEN
output <= <value>;
nx_state <= state2;
ELSE ...
END IF;
WHEN state2 =>
IF (input = ...) THEN
output <= <value>;
nx_state <= state3;
ELSE ...
END IF;
...
END CASE;
END PROCESS;
END <arch_name>;

## Slide 46: Example: BCD Counter

## Slide 47: Example: BCD Counter (II)
1 -------------------------------------------------
2 LIBRARY ieee;
3 USE ieee.std_logic_1164.all;
4 -------------------------------------------------
5 ENTITY counter IS
6 PORT ( clk, rst: IN STD_LOGIC;
7 count: OUT STD_LOGIC_VECTOR (3 DOWNTO 0));
8 END counter;
9 -------------------------------------------------
10 ARCHITECTURE state_machine OF counter IS
11 TYPE state IS (zero, one, two, three, four,
12 five, six, seven, eight, nine);
13 SIGNAL pr_state, nx_state: state;
14 BEGIN
15 ------------- Lower section: -----------------
16 PROCESS (rst, clk)
17 BEGIN
18 IF (rst='1') THEN
19 pr_state <= zero;
20 ELSIF (clk'EVENT AND clk='1') THEN
21 pr_state <= nx_state;
22 END IF;
23 END PROCESS;

## Slide 48: Example: BCD Counter (III)
24 ------------- Upper section: -----------------
25 PROCESS (pr_state)
26 BEGIN
27 CASE pr_state IS
28 WHEN zero =>
29 count <= "0000";
30 nx_state <= one;
31 WHEN one =>
32 count <= "0001";
33 nx_state <= two;
34 WHEN two =>
35 count <= "0010";
36 nx_state <= three;
37 WHEN three =>
38 count <= "0011";
39 nx_state <= four;
40 WHEN four =>
41 count <= "0100";
42 nx_state <= five;
43 WHEN five =>
44 count <= "0101";
45 nx_state <= six;
46 WHEN six =>
47 count <= "0110";
48 nx_state <= seven;
49 WHEN seven =>
50 count <= "0111";
51 nx_state <= eight;
52 WHEN eight =>
53 count <= "1000";
54 nx_state <= nine;
55 WHEN nine =>
56 count <= "1001";
57 nx_state <= zero;
58 END CASE;
59 END PROCESS;
60 END state_machine;

## Slide 49
Design Style #2 (Stored Output)

## Slide 50: Design Style #2 (Stored Output)
in design style #1 only pr_state is stored
In many applications, the signals are required to be synchronous, so the output should be updated only when the proper clock edge occurs
To make Mealy machines synchronous, the output must be stored as well
This structure is the object of design style #2
To implement this new structure, very few modifications are needed
we can use an additional signal (say, temp) to compute the output value (upper section), but only pass its value to the actual output signal when a clock event occurs (lower section).

## Slide 51: Design Style #1 vs. #2
Combinational
logic
Sequential
logic
input
clock
rst
nx_state
pr_state
temp
output
Style #1
Style #2

## Slide 52: Design Style #2 (Stored Output)
ENTITY <ent_name> IS
PORT (input: IN <data_type>;
reset, clock: IN STD_LOGIC;
output: OUT <data_type>);
END <ent_name>;
-------------------------------------------------------
ARCHITECTURE <arch_name> OF <ent_name> IS
TYPE states IS (state0, state1, state2, state3, ...);
SIGNAL pr_state, nx_state: states;
SIGNAL temp: <data_type>;
BEGIN
---------- Lower section: --------------------------
PROCESS (reset, clock)
BEGIN
IF (reset='1') THEN
pr_state <= state0;
ELSIF (clock'EVENT AND clock='1') THEN
output <= temp;
pr_state <= nx_state;
END IF;
END PROCESS;

## Slide 53: Design Style #2 (Stored Output)
---------- Upper section: --------------------------
PROCESS (pr_state)
BEGIN
CASE pr_state IS
WHEN state0 =>
temp <= <value>;
IF (condition) THEN nx_state <= state1;
...
END IF;
WHEN state1 =>
temp <= <value>;
IF (condition) THEN nx_state <= state2;
...
END IF;
WHEN state2 =>
temp <= <value>;
IF (condition) THEN nx_state <= state3;
...
END IF;
...
END CASE;
END PROCESS;
END <arch_name>;

## Slide 54: Example: String Detector
We want to design a circuit that takes as input a serial bit stream and outputs a ‘1’ whenever the sequence ‘‘111’’ occurs.
Overlaps must also be considered, that is, if . . .0111110 . . . occurs, than the output should remain active for three consecutive clock cycles.

## Slide 55: Style #2 Design of string detector

## Slide 56: Style #2 Design of string detector (Implementation)
5 ENTITY string_detector IS
6 PORT ( d, clk, rst: IN BIT;
7 q: OUT BIT);
8 END string_detector;
9 --------------------------------------------
10 ARCHITECTURE my_arch OF string_detector IS
11 TYPE state IS (zero, one, two, three);
12 SIGNAL pr_state, nx_state: state;
13 SIGNAL temp: BIT;
14 BEGIN
15 ----- Lower section: --------------------
16 PROCESS (rst, clk)
17 BEGIN
18 IF (rst='1') THEN
19 pr_state <= zero;
20 ELSIF (clk'EVENT AND clk='1') THEN
21 pr_state <= nx_state;
22 q<=temp;
22 END IF;
23 END PROCESS;

## Slide 57: Style #2 Design of string detector (Implementation)
23 ---------- Upper section: ---------------
24 PROCESS (d, pr_state)
25 BEGIN
26 CASE pr_state IS
27 WHEN zero =>
28 temp <= '0';
29 IF (d='1') THEN nx_state <= one;
30 ELSE nx_state <= zero;
31 END IF;
32 WHEN one =>
33 temp <= '0';
34 IF (d='1') THEN nx_state <= two;
35 ELSE nx_state <= zero;
36 END IF;
37 WHEN two =>
38 temp <= '0';
39 IF (d='1') THEN nx_state <= three;
40 ELSE nx_state <= zero;
41 END IF;
42 WHEN three =>
43 temp <= '1';
44 IF (d='0') THEN nx_state <= zero;
45 ELSE nx_state <= three;
46 END IF;
47 END CASE;
48 END PROCESS;
49 END my_arch;

## Slide 58
Traffic Light Controller (TLC)

## Slide 59: Traffic Logic Controller
Three modes of operation: Regular, Test, and Standby
  Regular mode: four states, each with an independent, programmable time, passed to the circuit by means of a CONSTANT
  Test mode: allows all pre-programmed times to be overwritten (by a manual switch) with a small value, such that the system can be easily tested during maintenance (1 second per state).
  Standby mode: if set the system should activate the yellow lights in both directions and remain so while the standby signal is active.
Assume that a 60 Hz clock (obtained from the power line itself ) is available

## Slide 60: Traffic Logic Controller (II)

## Slide 61: Traffic Logic Controller (III)

## Slide 62: Traffic Logic Controller Implementation (I)
5 ENTITY tlc IS
6 PORT ( clk, stby, test: IN STD_LOGIC;
7 r1, r2, y1, y2, g1, g2: OUT STD_LOGIC);
8 END tlc;
9 -------------------------------------------------
10 ARCHITECTURE behavior OF tlc IS
11 CONSTANT timeMAX : INTEGER := 2700;
12 CONSTANT timeRG : INTEGER := 1800;
13 CONSTANT timeRY : INTEGER := 300;
14 CONSTANT timeGR : INTEGER := 2700;
15 CONSTANT timeYR : INTEGER := 300;
16 CONSTANT timeTEST : INTEGER := 60;
17 TYPE state IS (RG, RY, GR, YR, YY);
18 SIGNAL pr_state, nx_state: state;
19 SIGNAL time : INTEGER RANGE 0 TO timeMAX;
20 BEGIN
21 -------- Lower section of state machine: ---
22 PROCESS (clk, stby)
23 VARIABLE count : INTEGER RANGE 0 TO timeMAX;
24 BEGIN
25 IF (stby='1') THEN
26 pr_state <= YY;
27 count := 0;
28 ELSIF (clk'EVENT AND clk='1') THEN
29 count := count + 1;
30 IF (count = time) THEN
31 pr_state <= nx_state;
32 count := 0;
33 END IF;
34 END IF;
35 END PROCESS;

## Slide 63: Traffic Logic Controller Implementation (II)
36 -------- Upper section of state machine: ----
37 PROCESS (pr_state, test)
38 BEGIN
39 CASE pr_state IS
40 WHEN RG =>
41 r1<='1'; r2<='0'; y1<='0'; y2<='0'; g1<='0'; g2<='1';
42 nx_state <= RY;
43 IF (test='0') THEN time <= timeRG;
44 ELSE time <= timeTEST;
45 END IF;
46 WHEN RY =>
47 r1<='1'; r2<='0'; y1<='0'; y2<='1'; g1<='0'; g2<='0';
48 nx_state <= GR;
49 IF (test='0') THEN time <= timeRY;
50 ELSE time <= timeTEST;
51 END IF;
52 WHEN GR =>
53 r1<='0'; r2<='1'; y1<='0'; y2<='0'; g1<='1'; g2<='0';
54 nx_state <= YR;
55 IF (test='0') THEN time <= timeGR;
56 ELSE time <= timeTEST;
57 END IF;
58 WHEN YR =>
59 r1<='0'; r2<='1'; y1<='1'; y2<='0'; g1<='0'; g2<='0';
60 nx_state <= RG;
61 IF (test='0') THEN time <= timeYR;
62 ELSE time <= timeTEST;
63 END IF;
64 WHEN YY =>
65 r1<='0'; r2<='0'; y1<='1'; y2<='1'; g1<='0'; g2<='0';
66 nx_state <= RY;
67 END CASE;
68 END PROCESS;
69 END behavior;

## Slide 64: TLC Simulation Result